TYMKRSCII, *.tciuser, 'Tim Kerski User File', Version 1

Description

A Tymkrscii User file is a binary file format used to store all of the settings and assets related to a single user.

The file is always of a fixed size, 8192 bytes long.

File Format

name	start	end	length	description

Header	0	15	16
User Logo	16	991	976	a user's logo
User Keys	992	3039	2048	a user's userkeys
User Site	3040	8191	5152	a user's badge site

Header Format

name	start	end	length	descriptions

File Type	0x00 -	0x08	9 Bytes	'TYMKRSCII'
Version	0x09 -	0x09	1 Byte	{tymkrscii_version}
Options	0x0A -	0x0F	6 Bytes	unused by the badge

User Logo

30x32 Mode 0 Tymkrscii Page File

If the user file was generated by the Imaginary Friend procedural generator built into the badge, the user logo will be the defaults/default.tcipage found on the badge.

If the user file was modified by the Logo Generator application found in the main badge menu, the user logo will be what ever was on screen when the user saved the logo.

If the user file was modified by the Uploader application found in the badge system menu, the user logo will be the custom.tcipage found in the root directory of the badge. The custom.tcipage may, in turn, have been generated using the Tymkrscii Draw python3 application found on your sdcard in the tools/ directory.

User Keys

MAX: 2048 byte Tymkrscii Key File

When extracted, the user keys section is treated as a linefeed delimited text file. Similar to how a .address can be used in the World File: an !address can be used in the user file keys to allow the badge adventure engine or browser engine to locate keys by name. Example:

!wallet
0
!calledmaude
yes

When packaging a Keys File into a User File: if the packager runs out of space while adding a line, then that truncated line is zeroed out back to the last line feed to avoid any corrupted lines from making it into the baked User File. If the last complete line begins with a '!' then that line is zeroed out as well to avoid the MagicInt from returning a line number past the end of the User Key Space.

If the user file is freshly generated by the Imaginary Friend procedural generator built into the badge, the user keys will be those found in defaults/default.tcikeys - with the USER_NAME_INDEX line changed to the output of the name generator.

If the Badge Adventure has been played, it may have modified other lines in the user file.

User Site

If the user file is freshly generated by the Imaginary Friend procedural generator built into the badge, the user site will be a copy of defaults/default.tcisite until being replaced by a custom.tcisite via the System Menu's Uploader Application.

MAX: 5152 byte Tymkrscii Site File

For more detailed information on site files, see the Badge Website Design Guide found on your sd card in the documentation/ directory.